## Slide 1
Memory BIST with Go-No-Go Testing for OR1200 System
Harsh Patel

## Slide 2: Agenda
    Project Overview
    Memory BIST Design Review
        Purpose
        Targeted Faults
        BIST Architecture (Design)
        Implementation & Results
    Synthesis & Timing Closure
    Instruction Cache & Data Cache
    Placement & Floorplan
    Challenges & Learning

## Slide 3: Project Overview
    Memory BIST (Built In Self Test) for OR1200
    OR1200 system
source: www.wikipedia.org/wiki/OpenRISC_1200

## Slide 4: Memory BIST Design Review
    Purpose / Motivation
Chart: 
| 1999 | 2002 | 2005 | 2008 | 2011 | 2014
% Area Logic | 60 | 30 | 14 | 8 | 4 | 2
%Area Reused Logic | 20 | 18 | 15 | 9 | 6 | 4
% Area Memory | 20 | 52 | 71 | 83 | 90 | 94
*source: ITRS 2011 & [1]

## Slide 5: Memory BIST Design Review
    Targeted Faults:
Fault Primitives
Multi-Port
Static
Dynamic
Simple
Linked
Simple
Linked
Struck-at
Coupling
Single Port

## Slide 6: Memory BIST Design Review
    BIST Architecture:

## Slide 7: Memory BIST Design Review
Pin Name | Pin Description
CLK | Clock for Memory/BIST
DATA | Input Data bus from the system
ADR | Address bus
WEN | Write/Read Enable
RST | Reset for Memory/BIST
TBIST | BIST Enabler signal that puts BIST between system and MEMORY When TBIST =1, BIST will be enabled. The actual Data, ADR & other CONTROL_PINS generation will start after 3 cycles (Sync phase) TBIST control can be managed from PoR sequence from system.
BBAD | Indicates the failures. Goes high as soon as detection of FIRST fault occurs and being 1 till the end of the testing; This is for GO-NOGO for SRAM; doesn't provide any debuggability.
BFAIL | Indicates the failures. Goes high every time whenever there is failure during the testing so corresponds to particular address of failure(debugging).

## Slide 8: Memory BIST Design Review
    Implementation
Input Generator
(Address , Data,
Rd/Wr Control)
Memory Under
Test
Output Comparator
&
Error Flag Generator
Algorithms (Hard coded)
+
Decoding Logic
+
Start/Stop Algo Control logic

## Slide 9: Memory BIST Design Review
    Implementation (Algorithm)
    March LR
    { (w0); (r0,w1); (r1,w0,r0,w1);
    (r1,w0); (r0,w1,r1,w0);
    (r0) }
    Fault Coverage:
Fault Name | Description
Struck-at 0/1 | The logic value of a stuck-at cell or line is always 0 (a SA0 fault) or always 1 (a SA1 fault).
Struck Open | The cell cannot be accessed; e.g. due to an open word line
Address Decoder Fault | 1. No cell access, 2. wrong cell access 3. multiple cells access.
Transition Fault | A cell fails to undergo a 0  1 transition and/or a 1 0 transition.
Data Retention Fault | A cell fails to retain its logic value after some period of time; this is caused in an SRAM by a broken (open) pull-up device
Coupling Fault | Transition of 01/10 in one cell impact the state of other near by cell.
Delay Decoder Fault | Transition from all address to its 1’s complement address

## Slide 10: Memory BIST Design Review
    Results:
    Synchronization & address/data/control signal generation.
    Algorithm change and corresponding data/address/read-write control

## Slide 11: Synthesis & Timing Closer
    Constrain writing
    Area vs. Time trade off
Synthesis Frequency (MHz) | Area(um2 )
200 | 1858.5454
250 | 
333.33 | 
500 | 
1000 ( Maximum achievable freq.) | 1930.8643

## Slide 12: Instruction & Data Cache
    Instruction Cache
        RAM
        TAG
    Or1200_ic_top.v

## Slide 13: Instruction & Data Cache
Combinational
Logic
ic_ram
ic_tag
ic_fsm
or1200_top
or1200_ic_top
BIST Wrapper

## Slide 14: Placement & Floorplan
    Prerequisites:
    Memory Macro (LEF/DEF/FRAM-CELL views)
      IC_RAM.def or FRAM view
      IC_TAG.def or FRAM view
    Synthesized net list of all individual modules
      BIST_IC_RAM_schematic.v
      BIST_IC_TAG_schematic.v
      ic_fsm_schematic.v
    Tried flow in two ways:
      1. Synthesis all individual blocks with dedicated constrains at block level integrate them at top.
      2. Synthesis of or1200_ic_top.v providing all hierarchical modules instantiated with global constrain (no hard boundaries)
       Option 2 is easy and fast if you don’t have power domain across modules. (no area/timing penalty for given global constrains)

## Slide 15: Placement & Floorplan
    Synthesis:
    P&R w/o Memory Macro:
    Final P&R w/ Memory Macro:

## Slide 16: Challenges & Learning
Design:
Clock domain crossing issue.
Memory testing algorithm implementation.
Verilog debugging.
Peripheral IP communication with your RTL.
Synthesis:
Constrains
Area and frequency trade-off
Critical path finding in case of slack violation and optimization in RTL.
Design w/ & w/o DFT feature – Area & Power comparision.
P&R and Integration:
Proper constrains is Big headache!!
Explore options for routing – Global routing, Track routing, Detailed Routing, Search & repair.
Memory LEF to DEF/FRAM conversation.
1 VSS was floating and couldn’t find which place it is in the design!!
Never ending some fuzzy DRC 

## Slide 17: References
[1] Challenges in Embedded Memory Design and Test, E. J. Marinissen et al. Proceedings of the Design, Automation and Test in Europe Conference and Exhibition (DATE’05)
[2] March LR: A Test for Realistic Linked Faults, Van de Goor et al. 14th VLSI Test Symposium 1996
[3] March SS: A Test for All Static Simple RAM Faults, Said Hamdioui et al. Proceedings of the 2002 IEEE International Workshop on Memory Technology, Design and Testing (MTDT 2002)
[4] Design of Generic Embedded Memory Built in Self Test Circuit, Qiao Liyan et al. The Ninth International Conference on Electronic Measurement & Instruments ICEMI’2009
[5] saed_mc_ug_v2.1.0, saed memory compiler user guide, synopsis.
[6] “How to Perform the Four Routing Stages in IC Compiler” – Synopsis
[7] Library Data Preparation for IC Compiler User Guide Version F-2011.09, September 2011
[8] IC Compiler User Guide: Implementation, Version B-2008.09, September 2008

## Slide 18
      Thank You!